## Slide 1: Prion Disease: BioRisk Evaluation Tool
Prepared by:
Ami Patel, PhD, RBP (ABSA)
Member – Emerging Infectious Diseases Committee (EIDC)
February 2025

## Slide 2
Hazard Identification | 
Pathogen | Prions
Host range | Mammals including humans
Occupational Health Risks and Considerations | • Family history of prion diseases • Eat meat infected by "mad cow disease" • Healthy individuals • No data on higher risk for individuals who are immunocompromised or have pre-existing conditions
Type of samples and proposed activities | Sample type: brain tissues, contaminated surgical tools Activities: • Laboratory work with prions (centrifuge, vortex, extraction, sharps), medical procedures (surgery) • Handling or preparing materials/slides for high-risk specimens (brain, Cerebrospinal fluid (CSF), Dura mater, Pituitary gland, Posterior eye (optic nerve and retina), Spinal cord and spinal ganglia, Trigeminal ganglia,
Additional information | Prions are discussed at length in BMBL 6th edition - Section VIII-H: Prion Diseases

## Slide 3
Pathogen Assessment | 
Factors | What is known
Biological agent | Prions - very novel type of infectious agent. PrP is a host-encoded protein, which exists as PrPC (cellular) in non-infected host and as PrPSc (scrapie) in infected host as infectious agent. Infectious prion proteins are derived from a conformational conversion of the normally folded prion protein (PrPC)
Disease | Prion Diseases or Transmissible spongiform encephalopathies (TSEs) • Scrapie in sheep • Bovine spongiform encephalopathy (BSE) in cattle • Chronic wasting disease (CWD) in cervids • Transmissible mink encephalopathy in mink • Creutzfeldt–Jakob disease (CJD) and variant CJD, Gerstmann-Sträussler-Scheinker syndrome (GSS), Fatal Familial Insomnia (FFI) in humans
Treatment | None
Transmission | In Humans: • Laboratory acquired infection • Direct contact with infected brain tissue • Iatrogenic - through medical procedures like organ transplants, surgery, and or through contaminated surgical equipment • Ingestion - eating meat of infected mammals
Host range | Mammals including humans
Infectious dose | Unknown; mathematical models suggests very low dose
Incubation time | Months to years for disease to develop.

## Slide 4
Threat Identification and Transmission |  | 
Category | What is known | Considerations
Laboratory/Environmental (Air/aerosols) | Not known to transmit as aerosols in humans. Aerosol transmission reported in immunocompetent mice in laboratory study (https://pmc.ncbi.nlm.nih.gov/articles/PMC3020930/) | 
Environmental (Water/Soil/) | Remain infectious after 3 years in soil. Likely to transmit via water. Known to naturally transmit via prion-contaminated food, milk, blood, saliva, feces and urine. | Prions in water: https://www.tandfonline.com/doi/full/10.4161/pri.3.3.9819 Prions in soil: https://journals.plos.org/plosone/article?id=10.1371/journal.pone.0000435
Personnel | Laboratory Acquired Infections (LAI) - ABSA LAI Database - https://my.absa.org/LAI; Several known LAIs in France and suspected LAIs in Italy | • Training on prion prior to laboratory work • Knowledge, Skills, Abilities • Availability of metal mesh gloves and specialized PPE when working with known, infected, or suspected prions and specimens • Dedicated or disposable material (PPE) and supplies for work with prions or suspected prion specimens • PPE and materials incineration and preferably not re-used
Waste | Consider type of biohazard waste: solid, liquid, sharps, mixed, etc. • Regulated medical waste resulting from surgery | Consider how waste is processed - autoclave on-site or through vendor?
Fomite | Medical or laboratory settings: Surgical instruments (electrical probes, metal equipment), surfaces where extensive handling of brain tissues occur | Consider potentially contaminated surfaces. E.g. surgical instruments, hospital or laboratory equipment, bench tops, storage, BSCs, etc.
Zoonotic | Significant animal to animal transmission occurring in nature through saliva, urine etc. Ingestion of contaminated food or milk from infected animals or use of contaminated animal-derived products | Animal infection with prions • Size of the animal, housing, waste management, allergies, shedding, husbandry • Necropsy, and handling /processing of infected brain tissues
Inactivation | Prions are unusual and highly infectious agents that are highly resistant to common decontaminants. Require harsh chemicals and higher concentration (e.g. 2N NaOH, 40% sodium hypochlorite), enzymatic digestion, or incineration. | Use prion-recommended disinfection practices (stronger concentration of bleach, higher and longer autoclave cycle, etc.). Incineration is highly recommended.

## Slide 5
Prevention Barriers
Hierarchy of Controls
Risk analysis for Prions
Engineering Controls
● Facility Design ● Negative or Unidirectional Airflow
● HEPA filters ● Building Alarms ● Monitors ● BSC ● Equipment
Administrative Controls
● Occupational Health Surveillance ● SOPs ● Staff training and competency ● Process validation ● Incident response
● Reporting ● Knowledge, Skills, Abilities ● Risk assessment
PPE and Laboratory Practices
● Appropriate PPE ● Type of laboratory procedures ● Best practices for pathogen containment ● Specific prion-recommended disinfection practices
THREAT
Agent
Source
Personnel
Waste Management
Fomite
Zoonosis (animal)
Facility
Security
HAZARD IDENTIFICATION
Agent
Host
Infectious dose
Procedure(s)
Frequency of exposure
TOP EVENT
[INCIDENT]
● Loss of primary containment ● Release into environment ● Cross contamination ● Loss of Control ● Breach in the chain of custody

## Slide 6
Mitigation and Post-Incident / Recovery Barriers
Risk analysis for Prions
Engineering Controls
● Early detection system ● Lock/disabling
Administrative Controls
● Exposure control ● Spill and emergency response ● Crisis management ● Health Surveillance (serology)
Safety and Laboratory Practices
● Follow SOPs ● Immediate reporting of incidents, accidents, and near-misses ● Ensure laboratory compliance ● Report new medical condition post exposure
HAZARD IDENTIFICATION
Agent
Host
Infectious dose
Procedure(s)
Frequency of exposure
TOP EVENT
[INCIDENT]
● Loss of primary containment ● Release into environment ● Cross contamination ● Loss of Control ● Breach in the chain of custody
CONSEQUENCES
USER/OPERATOR
Exposure
Illness
Diseases
Death
COMMUNITY
Distrust
Outbreak
ENVIRONMENT
Contamination
Transmission
INSTITUTION
Economic loss
Reputation

## Slide 7
Identification of Hazard
Pathogen
Personnel
Source/Host Range
Procedure
Frequency
Scale
Identification of Threat
Laboratory/Hospital
Waste Management
Fomite
Zoonosis
Inactivation
Identification of Consequences
Environment
Institution
Personnel
Community
Risk Assessment
Prevention
Mitigation
Risk Management
Elimination
Mitigation
Residual risk
Risk Management for Prions
Planned vs. Outcome
Indicators
Communications
Improvement
PERFORMANCE

## Slide 8
BioRisk Evaluation Tool (BET)
BET is designed to assist biosafety & biosecurity professionals to conduct risk evaluations
This tool may be used for risk assessments for various scenarios (i.e. laboratories, hospitals, etc.)
Select a hazard and use the BET to perform a systematic risk evaluation. The slide deck provides background information on Prions, prompts evaluation of hazards to conduct a thorough analysis, and provides a template for mitigation plan to address potential consequences (accidental or intentional).
Considerations when conducting a risk evaluation:
The outcome of the risk evaluation should be as robust as the hazard identification
Consider how each hazard can become a risk or threat
Determine the type of barriers that can prevent or mitigate adverse consequences
Identify the stakeholders associated with identified hazards and risks
This tool was prepared by Ami Patel as a member of EIDC. Special thanks to Joanna Spinato, Marian Downing, and Esmeralda Meyer for their time and input.

## Slide 9
References
https://www.pnas.org/doi/10.1073/pnas.172403799
https://pmc.ncbi.nlm.nih.gov/articles/PMC3156228/
https://pmc.ncbi.nlm.nih.gov/articles/PMC8404694/
https://www.science.org/content/article/france-issues-moratorium-prion-research-after-fatal-brain-disease-strikes-two-lab
https://absa.org/?s=prion
https://www.canada.ca/en/public-health/services/infectious-diseases/nosocomial-occupational-infections/creutzfeldt-jakob-disease/infection-control-guidelines.html
https://www.canada.ca/en/public-health/services/canadian-biosafety-standards-guidelines/handbook-second-edition.html
(Sections: 2.5 and 4.3.2 Prions, 12.13 Additional Equipment Considerations for Prions, 13.8 Special Considerations for Work with Prion-Infected Animals, 15.12 Additional Considerations for Prion Decontamination)
https://www.nejm.org/doi/full/10.1056/NEJMc2000687